◀ Back to (되돌아가기)

PC Interface Pin Assignment RS232C, Parallel (Printer port), USB, PS2, VGA

Copyright@ 2002 By Prof. Dr.-Ing. Hiesik Kim

| PC-interface / serial port connector pin assignment (RS-232-C) (25-pin) |
| --- |
| No. | Name | Function | from / to |
| 2 | TXD | sender, sending data out (+- 12V) | --> to receiver |
| 3 | RXD | receiver, receiving data in (+0V) | <-- from sender |
| 7 | GND | signal ground, common (0V) |  |
| 1 | Ground | chassis ground, shield (0V) |  |
| 4 | RTS | request to send out (+12V) | --> to CTS |
| 5 | CTS | clear to send in (+0V) | <-- from RTS |
| 20 | DTR | data terminal ready, out, (+12V) | --> to DSR |
| 6 | DSR | data set ready, out, (+0V) | <-- from DTR |
| 8 | DCR,/LSD | data channel received /line signal detected | <--> from & to DCR/LSD |

| 기능 | pin 번호 및 이름 |
| --- | --- |
| data communication | 2-TD, 3-RD, 7-Ground |
| handshaking | 4-RTS, 5-CTS, 20-DTR, 6-DSR, 8-DCR |
| wire connection: same line | Ground-Ground, chasis-shasis, DCR-DCR |
| cross connection | Rx-Trx, RTS-CTS, DTR-DSR |
| self-trick wire connection without handshaking | 5-4, 20-6 |

(RS-232-C) (9-pin)

3. TXD, sender, sending data out (+- 12V) ---> to receiver

2. RXD, receiver, receiving data in (+0V) <--- from sender

5. GND, signal ground, common (0V)

7. RTS, request to send out (+12V) ---> to CTS

8. CTS, clear to send in (+0V) <--- from RTS

4. DTR, data terminal ready, out, (+12V) ----> to DSR

6. DSR, data set ready, out, (+0V) <---- from DTR

1. DCR,/LSD, data channel received /line signal detected <----> from & to DCR/LSD

(RS-232-C) (6-pin)

1. TXD, sender, sending data out (+- 12V) ---> to receiver

3. RXD, receiver, receiving data in (+0V) <--- from sender

5. GND, signal ground, common (0V)

6. Ground, chassis ground, shield (0V)

2. DTR, data terminal ready, out, (+12V) ----> to DSR

4. NC, not connected, not used

| Printer port Centronics 25-pin assignment |
| --- |
| out | 2번,3번,4번,5번,6번,7번,8번,9번 |
| input | 10번,11번,12번,13번,15번 |
| in/out | 1번,14번,16번,17번 |
| gnd | 18,19.20,21,22,23,24,25번 |

(Centronics, Parallel interface, Printer Port) (36-pin)

1. strobe (-), synchronizing

2. data0, 3. data1, 4. data2, 5. data3, 6. data4, 7. data5, 8. data6, 9.data7

10. ack (-), pulse to acknowledge ready for more data

11. busy, can'not accept data more

12. PE, out of paper

13. Select, always high +5V

14.-16. NC

17. Fig, chassis ground

18. Reset (-)

19. -29. GND, Ground

30. -31. NC

32 error (-), no-paper, off-line, error

33.-36. NC

(Monochrom, CRT-Monitor) (9 pin)

1.-2. GND

3.-5. NC, Not connected

6. Intensity

7. Video

8. Horizontal Synchro

9. Vertical Synchro

(VGA, SVGA, color CRT-Monitor) (15 pin)

1. red video, 2. green video, 3. blue video

4. NC

5. self-raster

6. GND for red return

7. GND for green return

8. GND for blue return

9. NC

10.-11. ground (digital video)

12. NC

13. Hor.-synchro

14. Ver.-synchro

15. NC

(keyboard connector) (5 pin)

1. Ground

2. TxD, send data

3. RxD, receive data

4. +5V, power

5. NC

| <<Back to | 130-743 서울 동대문구 전농동 90 서울시립대학교 Ph.: 2210-2427, Lab: 2210-2569, HP: 017-311-2468, Fax.2213-8317 e-mail: drhskim 수정: 2002. April |
| --- | --- |